## Slide 1: Monte-Carlo studies for the drift velocity calibration measurement
Aleksei Dziuba / PNPI NRC KI
28th of May, 2020

## Slide 2: Calibration of drift velocities

## Slide 3: Conditions
720 GeV electrons as a beam
Simplified model
  Silicon detectors and scintillators at entrance and exit.
  Be windows
  H2, 20 atm as a single volume
Geant-4 with standard physics lists
Energy deposit at each tracking step is placed into a center of this step [should be improved]

## Slide 4: GEANT Model
720 MeV electrons
Be, 0.1 mm
H2 (20 atm.)
700 mm
y
z
Si, 0.25 mm
Scintillator, 10 mm
Si, 0.25 mm
Scintillator, 10 mm (removed in last versions)
+350 mm
-350 mm
This is simulation frame
50 mm gaps between detectors as well as between detector and berylliums
0 mm

## Slide 5: Energy deposit spectra from single electrons
Time protections (before and after signal) is assumed!  single electrons
Entrance scintillator
Exit scintillator

## Slide 6: Simulation of drift process and electronics
Simulation frame (x,y,z)  Main experiment frame (X,Y,Z)
  z  X; y  Y; x  Position – Z
Drift velocities:
  W1 = 3,08 mm / microsecond
  W2 = 7,50 mm / microsecond
Signal shaping as in test runs

## Slide 7: Flash ADC spectra (central anode pad, R=1cm)
Position = 50 mm; 10000 electrons
Mean = 17150.ns
Position = 250 mm; 1000 electrons
Mean = 81820. ns
Same ranges for y-axes

## Slide 8: Next steps
More realistic parameters (sizes, Wi, etc)
Improve ionization electron distribution
  Now all electrons are at the step center (DONE: Ionization along track )
Find robust estimator using toys. (CODE DONE) To check:
  Mean
  Mode
  Median
  Front
Other pads
Electronic noise
Check for different diffusion parameter in XY-plane
Use information from silicon detectors
What else ??? (New idea: Beam properties)

## Slide 9: Toy studies of different estimators
Central anode pad
Position = 250; Ne– = 1000; NToys = 100
Resolution is an RMS of estimator distribution
Different estimators:
  MeanFull 82016.8 +/- 41.0 ns
  MeanSigRegion 81122.7 +/- 9.1 ns
  Maximum 82016.8 +/- 10.8 ns
Signal region:
(Maimum-300 ch, Maximum+500 ch)
Other estimators is also possible to check

## Slide 10: Modification of the response functions
Current on anode appears, when an electron arrive to the grid.
It increases linearly and ends, when the electron reach anode.
T Grid-Anode = L Grid-Anode / W2
An integral of the current is the charge of one electron (e = 1.602176634×10−19 C).
Response function of pre-amplifier must be changed according to this process
Anode
Grid
1e–
0 mm
10 mm
L Grid-Anode
L Grid-Anode / W2
0
Current, A
Time, s
2 × e × W2 / L Grid-Anode

## Slide 11: New response function
Old
New
For the previous (“old”) simulation an electronic response appears, when an electron reach anode. Simple shift of the response function.
In a new version it starts, when an electron reach grid. Convolution with linear function (see previous slide).
Zero time – time, when electron is on the grid
L GridAnode = 10 mm; W2 = 7,5 mm/μs

## Slide 12: Spectrum with the new conditions
Conditions: W1= 4 mm/μs, L Grid-Anode = 10 mm
Position 250 mm, N Beam Electrons = 1000

## Slide 13: Longitudinal diffusion of electrons
σZ = 0,008 × √LTrackGrid
[σZ] = [LTrackGrid] = cm
Parametrization by German Korolev (private communication via Alexey Vorobyev)
Smear Z-position for each ionization electron by a Gaussian function with σZ.
LTrackGrid = 25 cm
10000 of beam electrons
With longitudinal diffusion
No diffusion

## Slide 14: Closer look
Ratio = No diffusion / With diffusion
Maximums are quite close
Toy studies are required for a quantitative answer.

## Slide 15: 100000 events
Maximum positions
With diffusion: 62317,9 ns
No diffusion: 62315,6 ns
2,3 ns difference

## Slide 16: All pads
1
3
2
5
4
6
7
9
8
10
15
14
12
13
16
11
Central pad is a circle with 1 cm radius
Others are half-rings with 4 cm width
Numbering as on sketch
X
Beam
0

## Slide 17: 50000 event
With and no diffusion options for all the pads
For each Flash ADC spectrum a bin of maximum as well as 10 bins to the left and 10 bins to the right are fitted with the polynomial of the 2nd order
No diffusion` With diffusion Difference
Pad 0 62318.8 62320.2 -1.43599 ns
Pad 1 62316.6 62318.2 -1.64263
Pad 2 62317.2 62318.7 -1.58292
Pad 3 62317.3 62318.8 -1.52238
Pad 4 62317.1 62318.6 -1.55779
Pad 5 62317.3 62318.9 -1.56173
Pad 6 62318.5 62320 -1.55719
Pad 7 62318.4 62320 -1.51919
Pad 8 62318.7 62320.2 -1.45737
Pad 9 62318.7 62320.2 -1.44617
Pad 10 62319.5 62321 -1.46183
Pad 11 62319.7 62321.1 -1.44189
Pad 12 62320.4 62321.8 -1.38731
Pad 13 62321.1 62322.5 -1.39093
Pad 14 62321.1 62322.4 -1.33407
Pad 15 62322.9 62324.2 -1.32674
Pad 16 62322 62323.3 -1.32055

## Slide 18: Increase diffusion parameter σZ by factor 4
25000 events / Same procedure as on previous slide
Difference in increased by factor of 10
No diffusion` With diffusion Difference
Pad 0 62319.1 62335 -15.9309
Pad 1 62316.4 62333.4 -16.9878
Pad 2 62317.1 62334 -16.9145
Pad 3 62317.2 62333.9 -16.6842
Pad 4 62316.8 62333.1 -16.3286
Pad 5 62317.8 62334.1 -16.2948
Pad 6 62318.8 62335.1 -16.2893
Pad 7 62319.3 62335.4 -16.1217
Pad 8 62318.4 62334.2 -15.8083
Pad 9 62319.4 62335 -15.6423
Pad 10 62319.6 62335.3 -15.6309
Pad 11 62320 62335.4 -15.3347
Pad 12 62321.4 62336.7 -15.3024
Pad 13 62320.8 62335.8 -14.9665
Pad 14 62321.4 62335.9 -14.445
Pad 15 62322.7 62337.1 -14.4829
Pad 16 62322.4 62336.6 -14.1763

## Slide 19: Different factors
Pad 0 (central circle)
Pad 16
Multiply diffusion parameter σZ by different factors
Almost linear dependence
Slope parameter is changing with the pad number
Pad 1

## Slide 20: Why peak position is pad –dependent?
Pad 1
Pad 16
500 beam electrons at Z=250 mm
Distribution of the ionization on different pads
Ionization size (width) is increasing with path in the H2

## Slide 21: Beam smearing with different material in front
1 cm material is placed on a 1st Scintillator place
Check Z-dependence (No-material, Carbon, Silicon, Copper, Silver and Tungsten)
Ionization spot become wider. See next slides.
Beam smearing with different materials doesn’t affect shift of the peak position due to diffusion
Worser precision (larger uncertainty) with the same statistics for different Z
Pad 7
Pad 16
Pad 1

## Slide 22: No material
1
2
16
15

## Slide 23: 1 cm of Ti
1
2
16
15

## Slide 24: Beam smearing in simulation
Beam is distributed uniformly in a circle of different radius
No visible effect of maximum position shift for “with” and “without” diffusion simulations
Pad 7
Pad 16
Pad 1

## Slide 25: Further studies of noise + simulation
See more details https://github.com/aleksha/G4-Models/tree/master/Data/Noise
Noise in data (baseline corrected)
Generated noise
Obtain distributions for real and imaginary part of frequency spectra using Fourier transformation;
Fit these distributions using two gaussian hypotheses;
Generate random spectrum out of these distributions;
Use inverse Fourier transformation to obtain spectrum of generated events.
Still to be implemented
We can have noise as a function of time!

## Slide 26: Energy calibration
5,5 MeV alpha-particle create a signal with integral of 200000 ADC channels (private communication with Alexander Inglessi)
A fake 1 mm track with 5,5 MeV energy deposit is created
It produces 150684 ionization electrons
Integral for the Flash ADC spectrum is 152022
1 electron has “weight” = (200000 / 152022)

## Slide 27: Flash ADC spectrum with noise (Pad 2)
10 beam electrons
100 beam electrons
1000 beam electrons
10000 beam electrons
Relative electronic noise is suppressed by an increase of the cumulative statistics
Current procedure is quite slow
½ noise event / second for one CPU core

## Slide 28: Cumulative noise baseline corrected spectrum
100k noise events
Is it a fluctuation or a problem?

## Slide 29: Fluctuations scales down
1k noise events
10k noise events
100k noise events
RMS = 8×10–5
RMS = 4×10–5
RMS = 3×10–5
NOTE: it isn’t and shouldn’t be a Gaussian distribution
Project cumulative distribution on its y-axis, which is scaled to averaged number (BinVal- AvVal) / AvVal

## Slide 30: Maximum shift due to noise
Peak is placed to the random location of cumulative noise spectrum
Shift of maximum for signal + noise (blue) wrt. pure signal (green)
Some fit examples

## Slide 31: Distribution for shift for 10k events
100 random places for signal peak at the noise spectrum. Signal shape at the peak region and cumulative noise spectra are same!
RMS for maximum with peak position fitting procedure 7,3 ns
Mean value for signals in the range ( Bin of maximum +/- 10 bins) is very dangerous estimator

## Slide 32: Distribution for shift for 100k events
100 random places for signal peak at the noise spectrum. Signal shape at the peak region and cumulative noise spectra are same!
RMS for maximum with peak position fitting procedure 5,1 ns
Mean value for signals in the range ( Bin of maximum +/- 10 bins) is very dangerous estimator

## Slide 33: Final model

## Slide 34: Final GEANT Model
720 MeV electrons
Ti, 0.5 mm
H2 (20 atm.)
700 mm
y
z
Si, 0.25 mm
Scintillator, 10 mm
Si, 0.25 mm
Scintillator, 10 mm (removed in last versions)
+350 mm
-350 mm
This is simulation frame
50 mm gaps between detectors as well as between detector and berylliums
0 mm
Ti, 0.5 mm
Beam is uniformly distributed in a circle with radius of 0,1 mm
No angular beam divergence!

## Slide 35: Distributions on pads
1
2
16
15

## Slide 36: Flash ADC spectra for 25k events (no noise)
Pad 01
Pad 16
No diffusion
With longitudinal diffusion

## Slide 37: 100k with noise
Pad 02
No diffusion
With longitudinal diffusion

## Slide 38
Only this pad contains electronics' noise
Only this pad contains electronics' noise
A scatter around a smooth curve indicates the accuracy of the estimate!

## Slide 39: Distribution for shift for 100k events
100 random places for signal peak at the noise spectrum. Signal shape at the peak region and cumulative noise spectra are same!
RMS for maximum with peak position fitting procedure 6,7 ns
Mean value for signals in the range ( Bin of maximum +/- 10 bins) is very dangerous estimator RMS = 17,9 ns)